## Slide 1
Audio in IP production
Andy Rayner, Chief Technologist, Nevion arayner@nevion.com +44 7711 196609
Come and catch up on the Sony stand in Hall 13

## Slide 2: Queen Elizabeth II 1926-2022
The Queen and I

## Slide 3: Don’t forget the audio- I am an sound guy!

## Slide 4: Distributed production
Event location or regional facilities
OB truck or local production
Central facility
Management
Public Cloud
5G
Home
Private Cloud

## Slide 5: IP transformation - Places, Processing & People
Notes: Our aim is to allow our customers to “create of compelling content anywhere, anytime and on any scale”.
We believe that requires our customers to be able to tap into the very best production resources everytime – the 3 Ps:
Places – ie. studios, control rooms, OB vans, etc
Processing – ie video and audio processing, such as switchers
People – i.e. the production team
Our mission is to enable all these resources to be included in the production, regardless of where they are.
How?

## Slide 6
Audio requirements drive scale in facilities
AUDIO -30

## Slide 7: The Audio folks did facility IP first!
‘Most of the complexity of a production environment is the audio’
Dante 2006 Ravenna 2010

## Slide 8: Audio facility interconnects
Remote commentary location
Event/ alternate
location
Production
Center
Re-sync
Re-sync

## Slide 9: History of sampling - PCM is 100 years old!
The First Disclosure of PCM: Paul M. Rainey,
"Facimile Telegraph System," U.S. Patent 1,608,527,
Filed July 20, 1921,
Determining sampling rate
Williard M. Miner, "Multiplex Telephony," U.S. Patent 745,734,
Filed February 26, 1903
Then Nyquist in 1924

## Slide 10: A-D conversion!
1954 "DATRAC" 11-bit, 50-kSPS Vacuum Tube ADC
Designed by Bernard M. Gordon at EPSCO
500watts, 150lbs, $8500
AD572 12-Bit, 25-μs Mil
Hybrid ADC, 1977

## Slide 11: Audio acquisition
Sample frequency
Bit depth
Time of capture

## Slide 12: Lots of different audio interfaces and formats!
Standardized Audio
interfaces
Standardized
IP formats
Proprietary
IP formats
Analogue
AES3
SDI embedded
IP 2022-6
embedded
IP - 3326
IP - AES67
AES10 MADI
Livewire
DANTE
RAVENNA
EBU 3326
AES67
ST2110-30/31
AES50
AoE
WheatNet
Q-LAN

## Slide 13: Audio production interoperability
Audio data flows – almost identical
Audio control plane – very different

## Slide 14: Audio parameters……………lots of choices
AES10 - MADI: 28, 56, 64 channels
Sample rate: 32kHz - 96kHz
Bit depth: 16bit, 20bit, 24bit
AES3: 2 channels
Sample rate: 16kHz, 22kHz,32kHz,44.1kHz,48kHz,88.1kHz,96kHz,192kHz
Bit depth: 16bit, 20bit, 24bit
AES3 frame period: 1ms – 12ms
AES67: 1 - 120 channels (1-8)
Sample rate: 44.1kHz, 48kHz, 96kHz
Bit depth: 16bit, 24bit
IP Packet period: 125us, 250us, 333⅓us, 1ms, 4ms
ST2110-30: 1-8 channels (1-64 channels Level C)
Sample rate: 48kHz (level A), 96kHz (level –x)
Bit depth: 16bit, 24bit
IP Packet period: 1ms (level A)125us (level B),

## Slide 15: The ST2110 suite & NMOS
SYSTEM -10
AUDIO -30
VIDEO -20
COMPRESSED VIDEO -22
AES3-32 bit AUDIO -31
TIMING -21
2022-8 COMPOSITE
ANCILLARY
DATA -40
MULTI-PART VIDEO -23
FAST METADATA -41
FMX -42
SD
VIDEO -24
IS-04
Discovery and Registration
IS-05
Connection Management
IS-08
Audio Channel Mapping
IS-07
Event and Tally
IS-09
System
BCP-003-0x
Security suite

## Slide 16: Handling ‘other’ audio: the ST2110-31 bits
AES3-32 bit AUDIO -31
AUDIO -30

## Slide 17: Timing and referencing
GNSS
GPS
TaaS
ST2059 – applying PTP IEEE1588 to media

## Slide 18: Origination time stamping in RTP
Media payload
RTP
UDP
IP
VLAN
MAC/PoS/ GFP/MPLS

## Slide 19
Audio per-sample timing
TS=n
TS=n+1
TS=n+2

## Slide 20
Time
e.g. 20ms
Video – per-frame sampling timing
ST2110-20 freezes RTP timestamp!

## Slide 21: What about the standardized control plane?
Audio data stream
Audio data stream
Controller
IS-04, IS-05, IS-08

## Slide 22: The SDP - RFC 4566 – used in ST2110
Sender description
Video and/or audio essence
Raster size (in pixels)
Frame-rate (video)
Channel count (audio)
Sampling structure (audio/video)
Bit depth (audio/video)
Colorimetry
Source IP address and port
RTP payload ID (audio/video)
PTP grandmaster source and domain
FAST METADATA -41
FMX -42
Coming soon

## Slide 23: Audio manipulation required in IP domain
GAIN
DELAY
DOWNMIX
SHUFFLE
IP
IP

## Slide 24: How to shuffle in the modern world
Mono AES67
Mono AES67
Mono AES67
Mono AES67
Mono AES67
Mono AES67
Mono AES67
Mono AES67
IP audio proc
AES67 1-64ch
AES67 1-64ch
AES67 1-64ch
AES67 1-64ch
AES67 1-64ch
AES67 1-64ch
AES67 1-64ch
AES67 1-64ch
End device selects
AES67 1-64ch

## Slide 25: Audio templates – a few practical options
One channel - mono
Two channels - stereo
Six channels – 5.1
Eight channels – 4 x stereo

## Slide 26: Video-associated audio format interfacing
ST 2022-6
16 Mono
ST 2022-6
16 Mono
ST 2022-6
16 Mono
ST 2022-6
16 Mono
ST2110-30
8 Mono
ST2110-30
8 Mono
ST2110-30
8 Mono
ST2110-30
8 Mono
SDI
16 Mono
SDI
16 Mono
SDI
16 Mono
SDI
16 Mono
ST 2022-6
16 Mono
ST 2022-6
16 Mono
ST 2022-6
16 Mono
ST 2022-6
16 Mono
ST2110-30
8 Mono
ST2110-30
8 Mono
ST2110-30
8 Mono
ST2110-30
8 Mono
SDI
16 Mono
SDI
16 Mono
SDI
16 Mono
SDI
16 Mono

## Slide 27: Audio-only format interfacing
2110-31
16 Mono
2110-31
16 Mono
2110-31
16 Mono
2110-31
16 Mono
2100-30
8 Mono
2110-30
8 Mono
2110-30
8 Mono
2110-30
8 Mono
Async in
16 Mono
Async in
16 Mono
Async in
16 Mono
Async in
16 Mono
AES3
16 stereo
Analogue
16 Mono
AES3
16 stereo
Analogue
16 Mono
AES67
64 Mono
AES67
64 Mono
AES67
64 Mono
AES67
64 Mono
MADI
64 Mono
MADI
64 Mono
MADI
64 Mono
MADI
64 Mono

## Slide 28: Moving outside the campus – distributed production
WAN connectivity involved
Longer latencies
(Potentially) Asynchronous sources
Layer 2 too limiting
Layer 3 (routed) needed for larger and multi-campus networks
PTP GM
PTP GM

## Slide 29: Interconnecting proprietary audio Islands
Plug and play ‘toolkit’ needed to transition to standardised formats
Gateway via ‘tie-lines’
SDN interconnect

## Slide 30: AES67 – defines link offset
link time

## Slide 31: Hybrid timing reconciliation
Processing time
Processing time
Processing time
Origination time
Use time
link time
link time
link time
link time
link time
Some chain timing preservation
Control system
Provides time coord

## Slide 32: PTP holdover is capable of being very long – let’s make it so!

## Slide 33: Protection – on and off campus – video & audio
n
n+1
n+2
n+4
n+5
n+6
n+8
n+9
n+10
n+3
n+7
n+11
n+12
n+13
n+14
n+16
n+17
n+18
n+20
n+21
n+22
n+15
n+19
n+23
n+24
n+25
n+26
n+27
n+28
n+29
n+30
n+31
n+32
n+33
n+34
n+35
n+36
n+37
n+38
n+39
n+40
n+41
n+42
n+43
(1,1)
(L,1)
(1,2)
(1,D)
(L,D)
(2,1)
(2,2)
1
L
2
flow A
flow B
SOURCE
DESTINATION
flow A
flow B
DESTINATION
SOURCE
delay
Spatial
Spatial + temporal
FEC

## Slide 34: International use case - Audio signal flows
Orchestration

## Slide 35: Secure networks need managed networks
SDN control

## Slide 36: Going off-campus – the IP facility media edge
PTP TIMING
DEVICE DISCOVERY & CTL
MEDIA FLOW IP ADDRESSING
UNCOMPRESSED ESSENCE FLOWS
PROTECTION TERMINATION
ALTERNATIVE TIMING DOMAINS
RESTRICTED/PROXY DISCOVERY & CTL
DIFFERENT IP ADDRESSING (NAT)
ESSENCE/COMPOSITE
UN/COMPRESSED FLOWS
PROTECTION TERMINATION
‘EXOTIC’ PROTOCOLS

## Slide 37: ST2110-WAN AG - two layers of focus – data and control
Media essences data flows
Registration, discovery and control

## Slide 38: ST2110-WAN
TR-09 Gateway G1
TR-09 Gateway G2
Facility 1
Facility 2
WAN
Encoding
Encryption
Error Protection
Encapsulation
CONTROL PLANE
DATA PLANE
Decoding
Decryption
Error Correction
Decapsulation
NMOS Resource Proxying
NMOS Resource Proxying
Notes: If we want to be able to share resources between different geographical locations in an interoperable way, we need standards and specifications that different manufacturers can all follow.
This is what the VSF’s ST 2110 over WAN group have been working on over the last couple of years. This will soon be published as TR-09.
We’ve tackled how to share 2110 media flows over a WAN both from the perspective of the data plane and the control plane.
For the data plane, considerations have included things such as:
- Encoding – compressing the media flows to save bandwidth whilst maintaining quality and low latency, using standards such as JPEG-XS
- Encryption – ensuring the data flows are secure
- Error protection – ensuring the data can get over the WAN even if the channel is less than perfect, using techniques such as forward error correction, RIST and 2022-7
- Encapsulation – ensuring that associated flows can arrive together across the WAN to assist synchronisation and to allow things like the forward error correction to be shared across flows. This is done by trunking the flows together.

## Slide 39: 2110-WAN control plane
TR-09 Gateway G1
TR-09 Gateway G2
Facility 1
Facility 2
WAN
CONTROL PLANE
NMOS Resource Proxying
NMOS Resource Proxying
Proxy Receiver
Proxy Receiver
Receiver
Sender
Proxy Sender
Proxy Sender
IS-04 Query API
IS-05 Conn API
IS-10 Auth API
Calls IS-04 Query API
Calls IS-05 Conn API
Calls IS-10 Auth API
Notes: For the control plane, we’ve proposed to use an NMOS-based approach.
We had several requirements:
- To allow only a subset of resources to be shared across the WAN, i.e. so Facility 1 can choose exactly which resources it shares with Facility 2 (we proxy resources using a Gateway to achieve this)
- To prevent Facility 2 from having any view of anything else going on in Facility 1 (Facility 2 only talks to the Gateway, nothing internal to Facility 1)
- To “not invent anything new” if at all possible (hence an NMOS-based approach using IS-04 and IS-05 with minimal additions and no required NMOS spec changes)
- To ensure all the control communications are secure, both in terms of being encrypted and in terms of authorisation - so that only an authorised second facility can access the control APIs of the first facility (using IS-10)
- To allow the method to be extendable to do things such as audio channel shuffling (using IS-08) or allowing a back channel control/tally path (using IS-07)
- To ensure each facility is autonomous and can run by itself without any dependence on the other facility - except for the shared flows of course (no interdependence)
- To ensure that no additional independent resources are required to be spun up in the WAN – everything resides is in one facility or the other and is accessed via the WAN gateway
- To ensure resources can be booked ahead of time (tags-based approach with current booking and booking list)

## Slide 40: The broadcast end game
Time-aware media processing chain
Acquisition
Consumption
Production
= real time & time aligned

## Slide 41: Deterministic data transfer Linear and non-linear
TCP
Infiniband
SRD
RTP/UDP
FEC
2022-7
ARQ

## Slide 42: In conclusion
Remote commentary location
Event/ alternate
location
Production
Center
Re-sync
Re-sync

## Slide 43: Thank you!
Andy Rayner Chief Technologist
arayner@nevion.com +44 7711 196609
Come and catch up on the Sony stand in Hall 13
Check out our other presentations on-line

## Slide 44
Any Questions?