## Slide 1
Timing planes in IP production linear and non-linear
Andy Rayner, Chief Technologist, Nevion arayner@nevion.com +44 7711 196609
Come and catch up on the Sony stand in Hall 13

## Slide 2: Queen Elizabeth II 1926-2022
The Queen and I

## Slide 3: The fundamental challenges
Linear connection-based signal flow
Non-linear compute-based data flow
Capturing time
Tracking time
Optimising time

## Slide 4: The relevant linear standards journeys
RFC 3550
RTP
RFC 4175
Uncompressed
video mapping
AES67
IP audio
VSF TR-03
ES media over IP
SMPTE ST 2210
RFC 768
UDP
SMPTE ST 292M
HD-SDI
SMPTE ST 424M
3G-SDI
IEEE 1588
PTP
SMPTE ST 2059 use of PTP
time

## Slide 5: The linear ST2110 suite (& NMOS ctl)
SYSTEM -10
AUDIO -30
VIDEO -20
COMPRESSED VIDEO -22
AES3-32 bit AUDIO -31
TIMING -21
2022-8 COMPOSITE
ANCILLARY
DATA -40
MULTI-PART VIDEO -23
FAST METADATA -41
FMX -42
SD
VIDEO -24
IS-04
Discovery and Registration
IS-05
Connection Management
IS-08
Audio Channel Mapping
IS-07
Event and Tally
IS-09
System
BCP-003-0x
Security suite

## Slide 6: The broadcast end game
Time-aware media processing chain
Acquisition
Consumption
Production
= real time & time aligned

## Slide 7: Why is ST2110-21 currently so critical?
IP Packet integrity
UDP
TCP
SRD
RoCE
Media payload
RTP
UDP
IP
VLAN
MAC/PoS/GFP/MPLS
IETF RFC3550

## Slide 8: Data transfer between Virtual Processing Functions
Deterministic data transfer
Media mapping
Media mapping
Compute does not do linear data transfer easily!

## Slide 9: Deterministic data transfer
TCP
Infiniband
SRD
RTP/UDP
FEC
2022-7
ARQ

## Slide 10: AWS CDI
SRD

## Slide 11: Reconciling media essence timings
Processing time
Processing time
Processing time
Origination time
Use time
link time
link time
link time
link time
link time

## Slide 12: The ST2110 suite & NMOS - revisions
SYSTEM -10
AUDIO -30
VIDEO -20
COMPRESSED VIDEO -22
AES3-32 bit AUDIO -31
TIMING -21
2022-8 COMPOSITE
ANCILLARY
DATA -40
MULTI-PART VIDEO -23
FAST METADATA -41
FMX -42
SD
VIDEO -24
IS-04
Discovery and Registration
IS-05
Connection Management
IS-08
Audio Channel Mapping
IS-07
Event and Tally
IS-09
System
BCP-003-0x
Security suite

## Slide 13: Timing propagation through system – ST 2110 revisions
RTP mode: NEW
T0
RTP mode: PRESERVE
Egress time point = t0+ta
RTP mode: PRESERVE
Egress time point = t0+ta+tb
RTP mode: NEW
Egress time point = t0+ta+tb+tc
Time plane is T1
Ta
= time from egress of previous device to time of egressing this device T1-T0 = TNEWRTP- TRTP
Tb
tc

## Slide 14: Example of production timing planes
Vision
Mixer
Audio
Mixer
Host Production
Replay
ISO
To File
Cam
Vision
Mixer
Package
Graphics
(match clock)
Program Pres
(unilateral)
Vision
Mixer
Cam
Studio
Channel
Presentation
Vision
And
Audio
Mixer
Mic
Audio
Mixer
Audio
Mixer
Mic
Mic
SSM
Camera
Playout
Commentary
File
Package
File
Data
Stats
Camera
Example drawing by Prin Boon, Phabrix

## Slide 15: Sources that cross timing planes
t0
Event Production switcher
Presentation switcher
ISO feeds also used directly

## Slide 16: Multiple production timing planes
t0
Final
Channel
playout
Remote control surfaces
Remote commentary
Event Production switcher
Presentation switcher
Remote/ Radio Cameras
!
Profanity delay
AR/VR set
time

## Slide 17: Specific real-world use-case in 2021
VR system
200ms

## Slide 18: VSF GCCG
Cloud <-> Ground
Cloud <-> Cloud

## Slide 19: The raster scan

## Slide 20: Linear broadcast technology

## Slide 21: Software procession execution time
tmax
Compute doesn’t easily do linear data handoff

## Slide 22: Compute latency and variability
Processing Step A
Processing Step B
Processing Step X
t
t
LAMIN
LA99%
t
LW99%
t
LXMIN
LX99%+LW99%
LX99%
Diagram courtesy of VSF GCCG AG

## Slide 23: Concatenated virtual processing functions, each with defined (max) execution time
VPF
1
VPF
3
VPF
4
VPF
5
VPF
2
t1
t2
t3
t4
t5
Time orchestration

## Slide 24: Same principles apply in virtualized world
Processing time
Processing time
Processing time
Origination time
Use time
link time
link time
link time
link time
link time
tmax
tmax
tmax

## Slide 25: Media Source timings
t0
Local
PTP-locked sources
Remote
PTP-locked sources
Transit delay – phase shift
t0
Asynchronous ‘rogue’ remote sources

## Slide 26: Proxy remote production timing reconciliation
Compressed lower resolution proxy images + audio (t=x)
Edit, mix, tally control data (t=y)
delay = transit time plus any compression etc
t+0
t+x

## Slide 27: Timing requirement examples
Audio-video Iip sync ~5ms
Coherent audio sync ~20us
Absolute time delivery ~20ms

## Slide 28: Hybrid timing reconciliation
Processing time
Processing time
Processing time
Origination time
Use time
link time
link time
link time
link time
link time
Some chain timing preservation
Control system
Provides time coord

## Slide 29: What is needed to make this work
Control system
provides time coordination
All media processing devices throughout chain provide necessary information and accept required configurations

## Slide 30: In-flight SMPTE RP/EG: ST2110-11
Draft an Recommended Practice document that defines a workable ecosystem to provide ‘automatic’ reconciliation of media essence timing at any point along a production chain.
Still time to get involved!

## Slide 31: Optimising latency
Frame n
Frame n+1
Frame n+2
Frame n+3

## Slide 32: The fundamental challenges
Linear connection-based signal flow
Non-linear compute-based data flow
Capturing time
Tracking time
Optimising time

## Slide 33: Back 13:00 Sunday & 10:30 Monday
IP networking tutorial
11:00 SUNDAY
Audio in live IP production
10:30 MONDAY
Notes: We are going to look at……

## Slide 34: Thank you!
Andy Rayner Chief Technologist
arayner@nevion.com +44 7711 196609
Come and catch up on the Sony stand in Hall 13

## Slide 35
Any Questions?