## Slide 1
ST 2110 Launch Pad
Jed Deame, CEO, Nextera Video

## Slide 2: Outline
What is NMOS?
Why do I need it?
How Does it Work?
Components
  IS-04 (Registration & Discovery)
  IS-05 (Connection Management)
  IS-07 (Event & Tally)
  IS-08 (Audio Mapping)
  IS-09 (System Discovery)
  BCP-003/IS-10 (Security)
  BCP-006 (NMOS for JPEG-XS/IPMX)
Why Should I Care?
How is it Going?
Example System
How Can I Try It?

## Slide 3: What is NMOS?
NMOS is the Networked Media Open Specification, developed by the Advanced Media Workflow Association (AMWA)
Delivered in the form of an open specification on the AMWA website
Enables ST 2110 Controllers and Devices to seamlessly interoperate across multiple vendors
Brings Plug & Play and Push-Button simplicity to Video over IP Routing

## Slide 4: Why do I need NMOS?
Required to route AV Signals from A to B
In SDI-land, every SDI router has a unique protocol
In IP, we have all agreed on NMOS
Alternative is lots of messy hand-editing of configuration files
NMOS is
  Auto-discovering
  Auto-configuring
  Multi-vendor Interoperable
  Push-button simple

## Slide 5: Why Should I Care?
During system provisioning, manually entering a sea of cryptic configuration options such as IP Addresses, Ports, PTP Parameters, etc. is time consuming, costly, and error prone
Plug and Play is a lot more Fun!
Most all new facility build tenders are specifying NMOS
Most Control System Providers have fully embraced NMOS
The EBU wants you to use NMOS

## Slide 6: EBU Mandate

## Slide 7: How do I know if a product supports NMOS?
Compatible Products Validated via the “JT-NM Tested” Program
Occurs every year, and provides comprehensive interop testing
over all aspects of NMOS, 2110, etc.
Results published at JT-NM.org

## Slide 8: How does NMOS Work?

## Slide 9: How is NMOS Accessed?
Through a set of Application Program Interfaces (APIs)
  In Plain English:
  http PUT/GET => http://<IP Address>/x-nmos /<API Name>/…
Examples (Viewable in Web Browser):
  http://192.168.10.2/x-nmos/node/v1.3/self
  http://192.168.10.2/x-nmos/query/v1.3/senders
  http://192.168.10.2/x-nmos/channelmapping/v1.0/map
  http://192.168.10.2/x-nmos/channelmapping/v1.0/outputs
  http://192.168.10.2/x-nmos/auth/v1.0/certs

## Slide 10: What is a Typical Implementation?
ST 2110 FPGA Core
ST 2110 Controller
PTP Grandmaster
ST 2110 Camera, GFX System, etc.
NMOS Core
PTP
Core

## Slide 11: Components

## Slide 12: IS-04 (Registration & Discovery)
Consists of 3 API’s
(Application Programming Interfaces)
Node API
Registration API
Query API
Registry
[PC running RDS SW or built into switch]
Node
[Camera, Monitor]
Contains a database of all NMOS devices on the network

## Slide 13: IS-05 (Connection Management)
IS-05 is an API which provides the means to create a connection between Senders and Receivers
Enables switching through “activations”
Activations can be immediate, relative, or absolute
Sender
Receiver
Activation
Now
In 5 seconds
At 12:00 PM

## Slide 14: IS-07 Event & Tally
“GPIO over IP”
  Camera Tally
  Dynamic Text (UMD)
  Etc.
Program
Tally
Tally
Lamp
Dynamic UMDs

## Slide 15: IS-08 (Audio Mapping)
Outputs
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16
Inputs
1-1
1-2
1-3
1-4
1-5
1-6
1-7
1-8
2-1
2-2
2-3
2-4
2-5
2-6
2-7
2-8

## Slide 16: IS-08 Demo – Audio Remapping

## Slide 17: IS-09 (System Resource)
Provides a global resource within the ST 2110 Environment
Located using DNS Service Discovery (DNS-SD)
Read by Media Nodes on Startup to determine:
  System ID (assigned randomly at each facility)
  Protocol (http or https)
  NMOS API versions supported
  PTP domain and announce interval
  RDS Heartbeat Interval
  Syslog hostname & port
Implementation Guide
  https://specs.amwa.tv/info-004/
IS-09
DNS-SD
Server

## Slide 18: NMOS Security
Confidentiality - Data passing between client and the APIs is unreadable to third parties.
Identification - The client can check whether the API it is interacting with is owned by a trusted party.
Integrity - It must be clear if data travelling to or from the API been tampered with.
Authentication - The client can check if packets actually came from the API it is interacting with, and vice versa.
Goals:

## Slide 19: Control Security
BCP-003-01
Encrypting communications between NMOS controllers & devices (https)
BCP-003-02
Client authorization and user management in NMOS systems
BCP-003-03
Certificate Provisioning using Enrollment over Secure Transport (EST)

## Slide 20: NMOS Security Example
Broadcast Controller
IP Source
Authorization Server
IP Destination
Auth Request
(OAuth)
Token
(JWT)
Essence Flow
(ST 2110)
Activation
(JWT)
Activation
(JWT)
Public Key

## Slide 21: BCP-006 (NMOS for JPEG-XS)
Enables ProAV applications to use NMOS
  To be supplemented by VSF TR-10-8 (NMOS for IPMX)
Refers to VSF TR-08 (Transport of JPEG-XS Video in ST 2110-22)
Leverages IS-04 & IS-05
Uses BCP-002-01 Natural Grouping
Uses media_type video/jxsv
Specifies updates to Session Description Protocol (SDP) file

## Slide 22: How is it going?
Early facilities adopting NMOS control had some issues (teething pains)
  Not all devices supported NMOS
  Some new NMOS devices didn’t get JT-NM testing (Covid)
  Controller specs not clear and Interop testing for controllers didn’t exist
Mitigation
  Most all new ST 2110 devices are support NMOS
  JT-NM Testing is back!
    Face2Face Interop August 19-23 @ Riedel (Germany), very productive
  AMWA INFO-005 Implementation Guide for NMOS Controllers
  Automated self-test suites NOW AVAILABLE for Devices & Controllers

## Slide 23: NMOS Testing
https://github.com/AMWA-TV/nmos-testing
https://github.com/rhastie/easy-nmos

## Slide 24: Example System

## Slide 25: IBC NMOS Demo 2110/IPMX/TR-08 Encode Universal Decode
KCU116 + VIDIO
4K (TX & RX)
NUC PC
Easy NMOS Registry
Matrox NMOS Controller
1080P HDMI
(Input 1)
4K HDMI
(Input 2)
AJA HD (TX)
Atomos 4k Player
4Kp50
HDMI
(Input 3)
HDMI
(MV Out)
3G
4Kp50
HDMI
(Input 4)
12G
HDMI
(1080p50/59
4Kp50)
ZCU106 (HDMI)
“Universal” 2110/IPMX (RX)
Atomos HD Player
Mellanox
Switch
VI VICO 4K IPMX (TX)
7th Sense 4K Player (TX)
4Kp50
4Kp50
4Kp50
HDp50
HDp50
ZCU106 (SDI)
“Universal” 2110/IPMX (TX)
12G Out
12G In
HDp50 2110
HDp50 IPMX
1080P
DisplayPort
(Input 5)
Source | Res | Format | KCU116 | ZCU106
7th | 4Kp25 | 2110 | • | •
VICO | 4Kp50 | TR-08 |  | •
AJA | 1080p50 | 2110 | • | •
Riedel | 1080p50 | 2110 | • | •
KCU116 | 4Kp50 | 2110 | • | •
ZCU106 | 1080p50 1080p50 | 2110 IPMX | • | • •
Decode
25G
Lynx
SDI-HDMI
AJA TX
Cobalt TX
Embrionix TX
AppearTV TX
7th Sense
VICO TX
Nextera 106 TX
Village Island TX
Nextera 116 TX
HDMI Multiviewer
IP Multiviewer
Source
Universal 2110/IPMX RX
KCU116 4K Decode
NMOS Switching Demo
Matrox
GUI
PTP
Grandmaster
Riedel HD (TX)

## Slide 26: Basic Controller - Riedel NMOS Explorer
https://www.riedel.net/downloads/firmware-software/

## Slide 27: NMOS Control GUI (Matrox ConductIP)

## Slide 28: NMOS Control GUI (Matrox ConductIP)

## Slide 29: Take-aways
NMOS IS-04 and 05 are solid, stable, and mature & offered in most all new ST 2110 products
NMOS Control Systems are greatly improved thanks to spec clarifications and interop testing
Features like IS-08 (Audio Mapping), IS-09 (System Discovery), and BCP-002 (Grouping) take NMOS to a new level, surpassing the level of control provided in SDI
BCP-003 (Security) adds a layer of security that has been sorely needed in control systems for quite some time
NMOS makes IP control easy, try it yourself!

## Slide 30
Any Questions?
Jed Deame marketing@nexteravideo.com
Please see our Live Demo in Hall 10, A26 (Next to EVS)