## Slide 1
Ground-to-Cloud Media Transport Integration - Standards and Approaches
John Mailhot – Imagine Communications
Kieran Kunhya – Open Broadcast Systems

## Slide 2
The integration of live signals into cloud-based production and playout applications across vendors brings unique challenges - hear about how the VSF is working to address these complex workflow requirements.
The integration of live signals into cloud-based production and playout applications across vendors brings unique challenges - the multitude of possible codecs, how to signal and find the endpoints, and making the transport robust against troubles. Within cloud-based workflows the fun really starts - how to send media signals between elements of a large-scale workflow such that the timing of the whole chain is managed - without replicating the traditional "frame-lock-step" approach we use on the ground. This session talks about the current work within the VSF to establish a flexible timing model and set of recommended practices for ground-to-cloud-to-cloud-to-ground workflows.

## Slide 3: What is Ground-cloud-cloud-ground (GCCG)?
Pandemic showed the power of the cloud to scale-up compute-heavy services on demand:
  Zoom, Cloud-hosted email, Social Media, Amazon, Netflix etc…
But television broadcast production still mainly on-premise – nearly all mid/high end production is some variant of in-person.
Cloud economics (scale-up/scale down) seems a great alternative to paying for resources that stay idle most of the time – what is stopping us?
Notes: Yes, it may go to a web platform but it’s produced in the same way as linear television

## Slide 4: Moving Cloud production to the next level
“But I’ve been doing live cloud production” – Yes and No
Single Vendor Monolithic applications such as Channel-in-a-box, playout server, cloud switchers, use the cloud as a home, but not necessarily as a scalable architecture
Proprietary Transports stifle innovation
To get widespread adoption we must have:
  Multi-vendor interoperation via standard APIs
  Appropriate-to-task picture quality levels
  Standards for Ground-Cloud-Cloud-Ground
  Agreed mechanism(s) for building workflows
Notes: Uncompressed to make sure no generation loss

## Slide 5: Cloud production – What makes it difficult?
Integration with the ground – both ways
  Must work into existing workflows
  SDI, ST 2110, satellite, cable, OTA
Legacy Workflows have well-defined linear timing models (e.g SDI, ST 2110-21, MPEG-TS VBV)
Without a proper timing model, you end up with variable (undefined) latency
  One reason web streams are 20-30 seconds behind broadcast – They don’t have a timing model!
  What are my neighbors cheering about?
Inter-cutting ground and cloud requires timing
Notes: Say, one stream has a one second delay and the other is two seconds

## Slide 6: I’ll just do 2110 in the cloud
Some people claiming to have 2110 in public cloud
But it’s not possible right now in any public cloud:
  No (full) PTP in the cloud – all clouds handle time their own way
  Cloud networks are shared and have packet loss
  No real access to network card capabilities (e.g packet pacing) for 2110
Is this even a good idea?
  We don’t actually want time-linear processing in cloud any more
  Allow cloud instances to process data non-linearly, sometimes faster or slower than real-time but on average real-time – known worst case
How to handle “synthetic” sources (e.g clips, graphics) played out from cloud?
Notes: Note, we don’t want linear processes in the cloud BUT we need to have linear output

## Slide 7: Cloud-vendor specific transport
To get the benefits of cloud, we also must trust the cloud
  Depend on cloud provider bulk-transport protocols
  Throughput with Reliability - all my data arrives correctly
  Latency - all my data will arrive on time
The Big Data community has similar needs for large data transfers
  Application may not have visibility of the internals of protocol (“black box”)
Amazon Scalable Reliable Datagram (SRD) such an example
Used in Amazon CDI

## Slide 8: Amazon CDI
How does the Amazon CDI protocol compare?
  Handles many of the challenges discussed
  An agreed way to exchange data between Amazon cloud instances. Defined pixel data structures, metadata (e.g HDR) etc
Amazon guarantees throughput, reliability and bounds latency
A big step forward for the industry
Some parts need GCCG input, more detailed timing model
GCCG could leverage CDI for applications where available (in Amazon)

## Slide 9: What is the VSF GCCG working group
The GCCG working group is Addressing this set of problems
The last difficult problem in broadcast production (personal view):
How can I do a complex multichannel production in the cloud, with comparable latency to on-premises and get it to the viewer?
Numerous technical challenges
https://vsf.tv/Ground-Cloud-Cloud-Ground.shtml

## Slide 10: Orchestration and Control
The boring but important part – on Ground and Cloud
How do cloud instances expose their capabilities (max resolution, frame rate etc.)?
Is there an orchestration layer that connects the pieces together?
Handling changes in signal flow (resolution/framerate, audio channels)
Connection status (Am I ready?)
Control of Ground to Cloud (and vice-versa) elements

## Slide 11: What are the “operating points” we see today (for TV)
Uncompressed (2022-6 or 2110-20) (already defined)
“PremiumCompressed” – super low latency, super high quality
  JXS for (1080i @ 200m?) (UHD @ 1000-1500M)
  Dual-path reliability model for super-good reliability @ minimum latency
J2K-ULL (stripes) @200
J2K (full-frame) @120
AVCI @ 100
Interactive Latency ~20Mbit(HD) (ULL restricted VBV buffer) $$
  ARQ/RIST or dual-path model or FEC? (Typical 4:2:2/10 profile)
Rate Optimized (longer latency @ lower rate) (HD@3-10 Mbits, more delay)
  ARQ/RIST or dual-path model or FEC? (Typical 4:2:0/8 profile)
Zoom / GoToMeeting / Webex – whatever gets a picture on the screen
  Internet best-effort reliability work
Focus on these
Work of the VSF GCCG AHG
Premium Compressed (JPEG XS)
VSF TR-08: codec & LAN 2110-22 base
VSF TR-09: WAN 2110-x extension
* reference TR-08
* opt: with 2022-7
* opt: with FEC (small intl, 1D)
* opt: GRE Tunnel (ref RIST)
* opt: encryption (ref RIST)
Interactive Latency (small GOP or Prog Refresh)
(HD) H264 (constrained VBV, 4:2:2, 10bit)
(UHD) H265 (constrained for latency)
2022-2(TS-RTP)
RIST-FEC (+/- multi-path)
Bandwidth Optimized
(HD) H264 (420/8 standard vbv)
(UHD) H265 ()
2022-2(TS-RTP)
ARQ or FEC
Opt: encryption (ref RIST)

## Slide 12: Where are the points-of-interoperability?
Ground-based Catcher
Ground-based Thrower
Cloud-side Thrower App
Cloud Production & Playout Apps
Cloud Production & Playout Apps
Cloud-side Catcher App
Unicast IP - WAN
UDP
GRE
-22
-30
-40
FEC/ARQ/-7
JXS
ANC
PCM
Live Source
Live Feed
Intra-Cloud Network
Cloud provider specific
Live Out
Cloud provider specific
Cloud provider specific
Cloud provider specific
Cloud provider specific
Cloud provider specific
encryption
UDP
GRE
FEC/ARQ/-7
Live Product
encryption
Signal Plane is the easy part
Unicast IP - WAN
TFS
TFS
TFS
Timestamped Formatted Samples
Timestamped Formatted Samples
Timestamped Formatted Samples
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
TFS
-22
-30
-40
JXS
ANC
PCM
Timestamped Formatted Samples
Timestamped Formatted Samples
Timestamped Formatted Samples
Ground
VSF TR-08 / TR-09 Interop Point
Interop Point
Interop Point
Interop Point
Work of the VSF GCCG AHG
Interop Point

## Slide 13: VSF and other Related Work In Progress
Document the “Premium Compressed” use case for G-C and C-G: TR-08 & TR-09
  TR-07 & 08 published. JPEG-XS over TS and over 2110-22 with interop points and capability sets
  TR-09 is publishing soon. Defines the data encapsulation plane, plus NMOS-like Control plane
Is there something more to document about the TS/IP/H.26x case? Or is it good enough?
  Can the TR-09 (ARQ, FEC, -7) control plane be applied to this class of streams ? (yes, probably)
Time-Flow / Time-Transport / Time-Tagging model
  How do we treat time in the concatenated virtualized systems
  How do we integrate “real-time” on the ground with “floating time” in the cloud?
  This requires a vocabulary and some modeling/specification effort
  Define how to catch up / manage drift / manage change / re-integration to timeline
The Media Containers / Object Format structures for hand-off from application to application
  The AWS CDI structures are defined on github
  Need to document how this handoff interacts with latency and latency accumulation
Work of the VSF GCCG AHG

## Slide 14: The “time variability / time floating” work
Allow variability in the handoffs, but with an ability to predict the outcome
Some processes must reconcile the variable inputs into a consistent output
  Must bound the input buffering (latency) yet accommodate the variability
What are the sources of delivery (arrival) variability?
  Network-induced (probably small)
  Processing-induced (upstream process steps with variable latency)
Vocabulary (about each process step in the datacenter)
  TX Variability – bound on how early/late the signal may egress, variance above baseline
  TX Planning Delay – the baseline in the above statement – the smallest value of delay
  Actual delay is planning delay plus some amount of variability
Work of the VSF GCCG AHG
How do we avoid re-creating our frame-sync pipeline in the cloud, and let software work well?

## Slide 15: What is the “spec” of latency and variability?
Push model (not backpressured)
Based on (uniform?) content “chunks”
  might be frames, fields, stripes
  might be blocks of audio samples
LMIN = the soonest/shortest amount of time from input to output
  Input time = buffer 100% arrived to me
  Output time = buffer left me 100%
  Includes the egress transit time
L99% = the amount of variability beyond the LMIN for 99th percentile case
What about continuity? Do processing steps need to maintain cadence if input not there?
  Maybe not – only if it “has to” for its own processing purposes. Otherwise best to just be late or missing and let downstream do the best it can with what it gets when it gets it.
Processing Step A
Processing Step B
Processing Step X
t
t
LAMIN
LA99%
t
LW99%
t
LXMIN
LX99%+LW99%
LX99%
Variability on the input accumulates into the output!!!
Work of the VSF GCCG AHG

## Slide 16: Summary of Consensus Views and path forward
For Ground-to-Cloud and Cloud-to-Ground, target TR08/TR09 for high-quality, and H.264/265 TS for intermediate quality
For inter-instance (intra-cloud) coordinated handoff (a “virtual facility”)
  Identify senders and receivers (use NMOS extended, similar to TR-09)
  Initiate connections (IS-05 extended) (WIP in AMWA BCP-06-x)
    What is the content description lingo? (VSF to recommend additions to AMWA)
    What are the transport params for CDI? for other clouds? (VSF will recommend to AMWA)
    What is the timing description specification? (document our WIP)
  What is the data format of the buffer-style handoff between instances in cloud?
    Canonical format = 2110 pgroup concatenated schema
    Other buffer formats can exist and may be more perfect, i.e. https://vsf-tv.github.io/cef/
    Canonical audio-only format including timing relationship and transport suggestion (TBD)
    Canonical metadata format including timing relationship and transport suggestion (TBD)
For inter-envelope (arms-length) handoffs within/between cloud(s)
  Essentially this is like the ground-to-cloud case

## Slide 17: Where do we go from here?
The VSF GCCG group has some WIP to document, and some actions to document/forward to AMWA
AMWA is extending NMOS to other stream types
VSF already published TR-08
VSF is publishing TR-09 very soon
Be sure to attend other talks this week about the sub-topics in here
Join the VSF and AMWA and help move this work forward

## Slide 18
Any Questions?