## Slide 1
JT-NM TESTED AUGUST 2022
JT-NM Tested Board Report
IP Media Equipment Testing For Interoperable Future

## Slide 2: CONTENT
What is JT-NM Tested?
What did we test and why?
Test plans and tools
Network and Infrastructure
Findings and results
Conclusions

## Slide 3
The JT-NM Tested program offers documented insight into how vendor equipment conforms to specific SMPTE standards and AMWA NMOS specifications.
Vendors who meet the testing criteria will have the opportunity to display badges and make public statements about their participation.
The JT-NM Tested Catalog lists vendor results along with a detailed test plan.
Anyone with the equipment listed in the test plan may execute the tests which were administered by the JT-NM test team, and you are encouraged to do so.
It is important to note that the JT-NM Tested program is not a certification program; rather, it is a snapshot in time of how vendor equipment conforms to key parts of SMPTE standards and AMWA NMOS specifications.
JT-NM Tested Program – What is it?

## Slide 4
3 main test tracks:
  Data plane: Network access and SMPTE ST 2110 behaviour (curated by EBU and VRT)
  Control plane: AMWA NMOS and JT-NM TR-1001-1 behavior, including NMOS registries and controllers (curated by EBU and CBC/Radio Canada)
  Cybersecurity Vulnerability Assessment (curated by EBU and VRT)
JT-NM Tested Program – What did we test?

## Slide 5
Test Plans:
  SMPTE ST 2110 Test plan
  NMOS/TR-1001-1 Test plan
  Cybersecurity Test Plan
Main testing tools:
  EBU LIST + multiple T&M devices
  AMWA NMOS Testing Tool
JT-NM Tested Program – Test Plans & Tools

## Slide 6
SMPTE ST 2110 Test Plan
NMOS / TR-1001 Test Plan
Cybersecurity Testing

## Slide 7
NETWORK AND INFRASTRUCTURE

## Slide 8
Objectives:
Provide a “real-world” scenario
Highlight ST 2110 network design best practice
Resilience and Reliability through design
Solution:
Spine-leaf topology, Amber and Blue media networks
Routed access
BGP Dynamic routing
Full multicast routing (IGMP / PIM)
Multiple management VLANs for general use and NMOS testing
Dual resilient PTP GMs
Routable OOB network for switch management
JT-NM Tested Program – Network and infrastructure

## Slide 9
16 switches in total:
  2x spine
  10x leaf
  4x OOB management
PTP:
  2x grandmasters by Telestream
DHCP:
  577x scopes
  Over 5000x lines in the config file
DNS:
  DNS-SD for NMOS registry discovery
NMOS registry:
  Easy-NMOS by Richard Hastie
JT-NM Tested Program – Network and infrastructure
Number of ports:
  48x 100G
  8x 40G
  116x 25G
  75x 10G
  215x 1G (Both media and management)
A strong move from 10G to 25G, and from 40G to 100G.

## Slide 10
FINDINGS AND RESULTS
https://jt-nm.org/jt-nm_tested/

## Slide 11
Data plane: Basic SMPTE 2110 behavior
Results of ST 2110 Testing (content by Willem Vermost, VRT)

## Slide 12
SMPTE ST 2110 Test Plan (content by Willem Vermost, VRT)
Network Tests
SMPTE ST 2110-20
SMPTE ST 2110-22
SMPTE ST 2110-30
SMPTE ST 2110-31
SMPTE ST 2110-40
SMPTE ST 2022-7
Download results and test plan!

## Slide 13
35 vendors published their results in the final catalog.
  +1 compared to the previous event
A few newcomers were welcomed
84 products were tested against the ST 2110 test plan (142% compared to previous catalog)
63 Video devices
  44 devices were presented as a UHD capable
  39 Tx/Rx devices
  13 Rx devices
  11 Tx devices
17 Audio only devices
  13 Tx/Rx devices
11K tests executed in total!
Results – SMPTE ST 2110 Test Plan (content by Willem Vermost, VRT)

## Slide 14
Network Interface Tests
  67% use DHCP on management network interface
  61% use DHCP on Media network interface
  99% respect the GM role when in “slave only”
  96% properly react to PTP TLVs
  57% warn or prohibit the use of the restricted multicast range (224.0.0.0-224.0.1.255)
ST 2110-10
  100% support and use IGMPv3 (*,G)
  67% support IGMPv3 SSM (S,G)
Results – SMPTE ST 2110 Test Plan (content by Willem Vermost, VRT)

## Slide 15
ST 2110-10
  67% expose and SDP
  93% of exposed SDPs were valid
ST 2110-20
  94% produce a valid stream
  94% produce a stream within the profile limits of N, NL or W
  86% Produce a stream within the boundaries of the VRX limits.
  92% can receive Wide streams
ST 2110-22
  25% of the devices demonstrated the ST 2110-22 capabilities
Lessons Learned – ST 2110 (content by Willem Vermost, VRT)

## Slide 16
ST 2110-30
  96% of the devices demonstrated capabilities for the ST 2110-30 tests
  77% have recommended DSCP values according to AES67
ST 2110-31
  39% of the devices demonstrated capabilities for the ST 2110-31 tests
ST 2110-40
  82% of the devices demonstrated capabilities for the 2110-40 tests
ST 2022-7
  88% of the devices demonstrated capabilities for 2022-7 tests
  58% had valid Seamless Protection Switching, critical for designing a resilient facility!
Lessons Learned – ST 2110 (content by Willem Vermost, VRT)

## Slide 17
Control plane: NMOS/TR-1001-1 behavior
Results of NMOS/TR-1001-1 testing (content by Felix Poulin, CBC/Radio Canada)

## Slide 18
NMOS/TR-1001-1 Test Plan (content by Felix Poulin, CBC/Radio Canada)
Startup Behaviour
Secure Communication (BCP-003-01)
Node API & Registration Behavior (IS-04)
Connection Management (IS-05)
Audio Channel Mapping (IS-08)
System Parameters (IS-09)
Receiver Capabilities
(BCP-004-01)
Download results and test plan!
NMOS Registry Tests

## Slide 19
17K tests executed - 92% automated!
Nodes
  74 Media Nodes +118% from 2020
  from 35 vendors + 75% from 2020
  87% of ST 2110 Devices tested for NMOS
  Growing adoption!
Capabilities
90% tests passed IS-04 Reg. and Discovery
65% do Natural Grouping (BCP-002-01)
8% do Receiver Capabilities (BCP-004-01)
91% tests passed IS-05 Connection Management
Maturity of most of IS-04 and IS-05 implementations!
Results – NMOS / TR-1001-1 Test Plan (content by Felix Poulin, CBC/Radio Canada)

## Slide 20
12% do basic or full Secure Communication (BCP-003-01)
  A beginning, but long way to go!
59% do System Parameters (IS-09)
19% do Audio Channel Mapping (IS-08)
76% do LLDP
Controllers and Registries
9 Controllers and Registries +29% from 2020
Capabilities
94% of Controller tests passed
66% of Registries partially supporting secured communication (BCP-003-01)
79% Registry tests passed (IS-04)
Results – NMOS / TR-1001-1 Test Plan (content by Felix Poulin, CBC/Radio Canada)

## Slide 21
CYBERSECURITY ASSESSMENT FINDINGS AND RESULTS
http://jt-nm.org/jt-nm_tested/

## Slide 22
Cyber Security – Early results straight from the oven of Gerben Dierick, VRT

## Slide 23
Cyber Security – Early results straight from the oven of Gerben Dierick, VRT

## Slide 24
EARLY CONCLUSIONS AND OUTCOMES
http://jt-nm.org/jt-nm_tested/

## Slide 25
It’s time for the EBU Pyramid revision.
JT-NM will look for a way to make the testing more automated and sustainable.
Extensive NMOS support is essential for future automatable testing. The value of the Badge must be revised and increased
The industry needs networking and PTP interop.
The cybersecurity situation hasn’t improved a lot – needs additional attention.
Another round of testing may take place in the Summer of 2023, with preparatory exercises to start soon.
Early conclusion and outcomes

## Slide 26
Thank you from the JT-NM Tested Team
https://jt-nm.org/jt-nm_tested/