## Slide 1
Kevin Salvidge – Leader Europe Limited
You don’t have to throw your SDI baby away with the bathwater.
End-user case studies on deployments of all sizes, as well as post-deployment considerations

## Slide 2: You don’t have to ……….
Disclaimer
The following presentations features real life events.
No customer have been named, to prevent any potential embracement.

## Slide 3: You don’t have to ……….
Reference Source
Unlike BB/TLS in the SDI world, PTP comes with a number parameters, that if incorrect configured, can result in unexpected an unpleasant affects to your IP operations.

## Slide 4
BMCA（ Best Master Clock Algorithm ）
  Who is Grandmaster?
  When devices powered on
  PTP Devices Listen
  Gather announce message
  Use BMCA to determine Grandmaster
  A key to the resiliency of the PTP is the BMCA.
  The BMCA allows a Leader to automatically become the Grandmaster or take over the duties of Grandmaster when the previous Grandmaster loses its GPS, gets disconnected due to a switch fault, or for what ever reason is unable to continue as Grandmaster.
Listening
Leader
Leader
Power up,
restart
Best Master Clock Algorithm
Announce
Announce
BMCA
Grandmaster
2110 Network
PTP-GM A
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 1
PTP-GM B
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 2
GPS Satellite
  Priority2: 1
Notes: BMCA runs on all devices
Grandmaster based on several parameters
  Priority - Lowest value wins (range 0-127)
  Clock Class
  Clock Accuracy
  Clock Variance
  Priority 2 Lowest value wins (range 0-127)
Final tie breaker
  Clock ID usually MAC address (media access control address) 00:09:0D:xx:xx:xx = Leader Electronics

## Slide 5
PTP １
PTP ２
DOMAIN 127
DOMAIN 0
ST2059
PROFILE
AES67 PROFILE
System configuration with Domain divided
  Some audio equipment only supports the profile of AES 67
Video equipment
Audio equipment
Domains are for use of multiple PTP services simultaneously with one physical Ethernet connection.
PTP operation is performed between devices having the same DOMAIN.
Domain 0 is used by Audio services for audio reference.
Domain 127 is the default for PTP, so any new equipment that is added to the network could be a Grandmaster via BMCA on Domain 127, so it is possible to have the new equipment take over without you knowing it.
DOMAIN 44
PTP Domains

## Slide 6
Leader
Best Master Clock Algorithm
2110 Network
PTP-GM A
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 1
PTP-GM B
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 2
Grandmaster
BMCA
GPS Satellite
If the Leader does not see an Announce message from a better clock within the Announce Time Out Interval, then it takes over the role of Grandmaster.
Notes: After power up the first thing the clock does is ‘listen’, in other words it looks for Announce messages from the PTP general multicast address. An Announce message contains the properties of the clock which sent it.
If the Ordinary Clock sees an Announce message from a better clock, it goes into a ‘Follower’ state, or passive if its not slave capable.
If the Ordinary Clock does not see an Announce message from a better clock within the Announce Time Out Interval, then it takes over the role of Grandmaster.
This runs continuously so master capable devices are constantly on the look out for the possible lose of the current master clock.
For this reason, it is critical that the Announce Time Out Interval be set longer than the Announce Interval in your network.
If you don’t then master capable devices will keep jumping to the conclusion that the master has gone away and they need to take over.

## Slide 7
Leader
Best Master Clock Algorithm
2110 Network
PTP-GM A
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 1
PTP-GM B
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 2
Grandmaster
BMCA
GPS Satellite
This runs continuously so Leader capable devices are constantly on the look out for the possible loss of the current Grandmaster.
Notes: After power up the first thing the clock does is ‘listen’, in other words it looks for Announce messages from the PTP general multicast address. An Announce message contains the properties of the clock which sent it.
If the Ordinary Clock sees an Announce message from a better clock, it goes into a ‘Follower’ state, or passive if its not slave capable.
If the Ordinary Clock does not see an Announce message from a better clock within the Announce Time Out Interval, then it takes over the role of Grandmaster.
This runs continuously so master capable devices are constantly on the look out for the possible lose of the current master clock.
For this reason, it is critical that the Announce Time Out Interval be set longer than the Announce Interval in your network.
If you don’t then master capable devices will keep jumping to the conclusion that the master has gone away and they need to take over.

## Slide 8
Leader
Best Master Clock Algorithm
2110 Network
PTP-GM A
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 1
PTP-GM B
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 2
Grandmaster
BMCA
GPS Satellite
For this reason, you want the network detection timeout to be longer that the Time out interval of the BMCA (Grandmaster / Leader)
Notes: So the GM can timeout and change #2 GM but the network does not time out and do a double change.

## Slide 9
Leader
Best Master Clock Algorithm
2110 Network
PTP-GM A
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 1
PTP-GM B
  Domain: 44
  Priority1: 1
  ClockClass: 6
  Priority2: 2
Grandmaster
BMCA
GPS Satellite
If you don’t, then the Leader capable devices will keep jumping to the conclusion that the Grandmaster has gone away and they need to take over.
Announce
Grandmaster
Leader

## Slide 10
Spine
Leaf .
In an Air Gap Network the only connection between networks is the PTP communication between the two Grandmaster and the Leader
Each South bound Leaf Port is a Boundary Clock
BC
BC
BC
BC
BC
BC
Each Leaf connects to every Spine in it own network
PTP Only Interconnect
VLAN
Need more Nodes add more Leafs
Need more Bandwidth add more Spines
NOTE: For Spine / Leaf network architectures the Leaf ports connected to PTP follower endpoints should always stay in Master state.
Configure this CLI to ensure they will always stay as masters, even if the Follower is misconfigured or a GM is accidently connected under this port.
Larger 2110 Leaf and Spine
Ensure the BMCA elections take place at the feeder switch level not lower down the media network
Notes: NOTE: For Spine / Leaf network architectures the Leaf ports connected to PTP follower endpoints should always stay in Master state.
Configure this CLI to ensure they will always stay as masters, even if the Follower is misconfigured or a GM is accidently connected under this port.

## Slide 11
Best Master Clock Algorithm

## Slide 12
Backup
SPG
Primary
SPG
ECO
Analog
BB
Analog
BB
Analog
Tri-Level Sync
Analog
Tri-Level Sync
SD/HD
SDI
Black
SD/HD
SDI
Black
Digital Audio
AES/EBU
Reference
Digital Audio
AES/EBU
Reference
To
Distribution
Amplifiers
Sync Pulse Generators (SPG’s)
Notes: Dual master reference SPGs are used with an emergency changeover unit (ECO) as shown.
The ECO is able to detect a loss of sync signal at its master input and automatically switch to the back-up input.
Maintaining the sync signal at the output of the ECO prevents a loss of a critical sync signal from affecting timing within the plant.
Synchronization throughout a facility is a critical operation for guaranteed system performance, which is why designing a facility with redundant synchronization provides a complete fault-tolerant, flexible, and robust system.
In many broad- cast and post-production facilities, Emergency Change- Over units such as the Leader LT4448 are used to automatically switch from one sync source to another upon fault detection in any active source without loss of service within a facility.
The LT4610/11 can be used in combination with another LT4610/11 unit to provide a back-up in case of failure of one of the components within the timing system. The LT4448 has eleven user-configurable channels and can be configured to support analogue Black Burst (PAL or NTSC), HD tri-level sync, AES/EBU digital audio, SD-SDI and HD-SDI.
After completing the timing set-up of the whole facility, it is important to save the settings of the Master and Slave SPG.
The LT4610/11 allows the devices configuration to be saved to a USB memory device. This feature is useful when you want to duplicate LT4610/11 settings on multiple LT4610/11 devices.
To alleviate further concerns for loss of house timing reference signals, an uninterruptible power supply (UPS) should be incorporated into the system. This prevents power surges or brief loss of power from interrupting the output configurations of the SPG and interfering with the timing settings for the system.
This configuration of a UPS, LT4448 ECO and SPGs ensure peace of mind and could prevent problems if a power failure occurs.

## Slide 13
ECO
Analog
BB
Analog
BB
Analog
Tri-Level Sync
Analog
Tri-Level Sync
SD/HD
SDI
Black
SD/HD
SDI
Black
Digital Audio
AES/EBU
Reference
Digital Audio
AES/EBU
Reference
To
Distribution
Amplifiers
PTP – SMPE ST 2059 / AES67 / General
To
Network Switch
PTP – SMPE ST 2059 / AES67 / General
To
Network Switch
Backup
SPG
Primary
SPG
Sync Pulse Generators (SPG’s) + PTP
GrandMaster
Notes: You will still have the ECO for SDI, AED and black, but an ECO is not used for the PTP. PTP uses a voting system called BMCA

## Slide 14
ECO
Analog
BB
Analog
BB
Analog
Tri-Level Sync
Analog
Tri-Level Sync
SD/HD
SDI
Black
SD/HD
SDI
Black
Digital Audio
AES/EBU
Reference
Digital Audio
AES/EBU
Reference
To
Distribution
Amplifiers
PTP – SMPE ST 2059 / AES67 / General
To
Network Switch
PTP – SMPE ST 2059 / AES67 / General
To
Network Switch
Backup
SPG
Primary
SPG
Sync Pulse Generators (SPG’s) + PTP
GrandMaster
GrandMaster
X
Notes: You will still have the ECO for SDI, AED and black, but an ECO is not used for the PTP. PTP uses a voting system called BMCA

## Slide 15
LT4610 Primary
LT4610
Primary
GPS
GPS
LT4610
Secondary
PTP trunk
BB
RJ45 or SFP+
LT4448
Change Over
BB
BC
LV5600
RJ45 or SFP+
Primary Network
Secondary Network
BB
BC
SNMP Controller
For SNMP
Get Primary LT4610 Status.
(Lock status, Clockclass, etc.)
Get Backup LT4610 Status.
(Lock status, Clockclass, etc.)
Set Change Over.
Primary to Backup
Sync Pulse Generators (SPG’s) + PTP

## Slide 16
ECO
Analog
BB
Analog
BB
Analog
Tri-Level Sync
Analog
Tri-Level Sync
SD/HD
SDI
Black
SD/HD
SDI
Black
Digital Audio
AES/EBU
Reference
Digital Audio
AES/EBU
Reference
To
Distribution
Amplifiers
PTP – SMPE ST 2059 / AES67 / General
To
Network Switch
PTP – SMPE ST 2059 / AES67 / General
To
Network Switch
Backup
SPG
Primary
SPG
Sync Pulse Generators (SPG’s) + PTP
GrandMaster
Analog
Tri-Level Sync
X
Analog
BB
SD/HD
SDI
Black
Digital Audio
AES/EBU
Reference
GrandMaster
Analog
BB
Analog
Tri-Level Sync
SD/HD
SDI
Black
Digital Audio
AES/EBU
Reference
Backup
SPG
Primary
SPG
Notes: You will still have the ECO for SDI, AED and black, but an ECO is not used for the PTP. PTP uses a voting system called BMCA

## Slide 17: You don’t have to ……….
Ancillary Data
Over the years, the SDI “Ancillary Data” system has become the home for lots of things.
  Some are intrinsic to the video signal
  Some are independent essences
  And some have ended up there because it seemed like a good place to put it at the time.

## Slide 18: You don’t have to ……….
Video Payload ID (VPID) Codes
SMPTE ST352
Is carried within the Ancillary data space to assist a device in quickly decoding the video signal.
SMPTE ST2110-20 specifies the transport of uncompressed active video
The Ancillary Data is managed as part of SMPT ST2110-40
Notes: One of those Ancillary Data essences that is intrinsically linked to the video signal is the video payload ID

## Slide 19: Video Payload ID
Notes: And for any engineer who has time fault finding a system the ‘Magic decoder ring’, as it is sometimes referred to is vital when it comes to fault-finding systems in SDI.

## Slide 20
And now for a new challenge !
To assist in the control and switching of IP multicast flows within a broadcast facilities broadcasters are using NMOS Orchestration systems to configure IP receivers.
They configure receivers by means of Session Description Protocol (SDP).
Session Description Protocol does not deliver any media streams itself but is used between endpoints for negotiating on network metrics, media types and other associated properties.
You don’t have to ……….

## Slide 21
Session Description Protocol
  Video
  Audio
  ANC Data
You don’t have to ……….
-20 Video
-30 Audio
-40 ANC

## Slide 22
Session Description Protocol
You don’t have to ……….

## Slide 23
You don’t have to ……….
Session Description Protocol
Being able to analysis the SDP is vital if an error has occurred in its creation and receivers on the network are unable to connect or display the IP stream.
The SDP can be copied and exported as a text tile for remote analysis.
SDP - Video
SDP - Audio
SDP - ANC

## Slide 24
You don’t have to ……….
Session Description Protocol
In ‘True Hybrid’ operation, the Leader can display both the SDI Payload ID and the SDP to allow easy comparisons.
SDI Video Payload ID
SDP Video Payload ID

## Slide 25
You don’t have to ……….
Session Description Protocol
The same applies to ANC Data Analysis of -40 ANC Data stream and SDI embedded audio

## Slide 26
You don’t have to ……….
Day-to-Day Operations
‘True Hybrid’ operation allows you to ensure ancillary data like closed captions are present.
Multiple analysis tools like PIC and WFM can be displayed in both IP and SDI.
608 Captions
608 Captions

## Slide 27
You don’t have to ……….
Day-to-Day Operations
The same applies to Audio Analysis of -30 or -31 audio stream and SDI embedded audio.
Surround Channels missing

## Slide 28: You don’t have to ……….
IP to SDI Gateways
Test and Measurement products have always acted as gateways in broadcasters’ facilities.
Now, with the introduction of IP, they are continuing to fulfil this role.

## Slide 29
4x 3G-SDI Output
Professional Broadcast Monitor
Link - 1
VPID
Both the LV5600 and LV7600 can convert IP Streams to SDI video and insert VPID
You don’t have to ……….
Notes: SDI Out PID Insert – When set to on, the Payload ID format information is inserted into the SDI output converted from IP to SDI.
The Payload ID can either be sourced from the ST.2110-40 stream, NMOS(SDP) or manual.
The 4K input signal is converted to 3G-Quad Link, so the 3G Quad Link payload ID is inserted.
When set to off, if the PayLoad ID is inserted in ST2110-40, that information is inserted. When Type is set to ST2110, this can be selected.

## Slide 30: You don’t have to ……….
Vision Engineer in an IP World
It’s not uncommon for Vision Engineers to have to control multiple cameras and this involves rapidly switching between cameras sources.

## Slide 31
You don’t have to ……….
Day-to-Day Operations
Vision Engineers expect the same performance from IP test and measurement products, as they previously enjoyed with SDI.
They also don’t care if the video source is IP or SDI, their job is to match the images, irrespective of underlying infrastructure.

## Slide 32: You don’t have to ……….
Audio-to-Video Synchronization
Also known as lip sync refers to the relative timing of audio (sound) and video (image) parts during playout.
Notes: Broadcasters have had a love / hate affair with lip sync from day one.
With Analogue video and audio, the independent essences were subjected to different propagation delays, depending on the path of the signals.
With SDI, that issue kind of went away when the audio was embedded into the serial digital stream.
Then, with UHDTV the problem re-appeared, especially is broadcasters used square-division, as delays had to be introduced to manage the processing of four HD images.
Now, with SMPTE 2110, we are back to the point we were with analogue video and audio, namely the propagation delays in the path the essences take can impact the final playout.

## Slide 33
You don’t have to ……….
Day-to-Day Operations
It can be confirmed whether video, audio and ANC essences are synchronized with PTP by comparing the timing information of the PTP and the RTP timestamp.
The transmitting side transmits the stream according to the time of the PTP and the receiving side reproduces in accordance with the time of PTP.

## Slide 34
PTP Master
Vision Mixer
Audio Mixer
You don’t have to ……….
PTP Master
RTP Timestamp
RTP Timestamp
Propagation Delay
Video
Audio
PTP

## Slide 35
PTP Master
Vision Mixer
Audio Mixer
You don’t have to ……….
RTP Timestamp
RTP Timestamp
Propagation Delay
Video
Audio
PTP
HDR<>SDR
UHD<>HD
RTP
Timestamp
RTP
Timestamp
Propagation Delay
?
PTP Master
Notes: If the -20 Video stream is then subject to additional processes, like HDR<>SDR conversion or UHD<>HD conversion, these processes take time and at the end of each process the -20 video stream has a new RTP Timestamp.
But whilst the -20 Video streams are undergoing these processes, the -30 / -31 Audio streams arrive at the transmission input ahead of the -20 Video stream and thus we have an Audio-to-Video Synchronization

## Slide 36
You don’t have to ……….
Day-to-Day Operations
Using an IP AV Delay test pattern allows broadcasters to accurately identify the AV Delay.
The IP AV Delay Graph displays the Audio Lead/Lag for each individual audio channel.
IP AV Delay Test Pattern
Audio Bars
IP AV Delay Graph

## Slide 37
You don’t have to ……….
AV Delay

## Slide 38
You don’t have to ……….
PTP Timing Comparison
Notes: The PTP timing comparison screen shows the comparison of the timings of the RTP video, audio, and ancillary signals relative to the PTP.

## Slide 39
PTP Master
Vision Mixer
Audio Mixer
You don’t have to ……….
Video
Audio
PTP
HDR<>SDR
UHD<>HD
RTP
Timestamp
RTP
Timestamp
Propagation Delay
PTP Master
Notes: If the -20 Video stream is then subject to additional processes, like HDR<>SDR conversion or UHD<>HD conversion, these processes take time and at the end of each process the -20 video stream has a new RTP Timestamp.
But whilst the -20 Video streams are undergoing these processes, the -30 / -31 Audio streams arrive at the transmission input ahead of the -20 Video stream and thus we have an Audio-to-Video Synchronization

## Slide 40
You don’t have to ……….
Notes: If you are here in Las Vegas for IBC 2022 and would like to discuss further any of the subjects I’ve just been talking about, please drop by the Leader booth in Hall 10 Stand C01.

## Slide 41
Building a foundation of shared knowledge and practical experience in the area of IP media networking
Visit the Education Library at AIMSAlliance.org
Let us know what training and learning opportunities you’d like to see in the field of IP Media Networking
info@aimsalliance.org
AIMS Education Working Group

## Slide 42
Kevin Salvidge
  Sales Engineering Manager
  Email : salvidge@leadereurope.com
  Tel : +44 7826 178 752
You don’t have to ……….
Notes: Or, if you are not at the show, but would like to contact me, please feel free to use the contact details on the screen.

## Slide 43
If you would like more information including a copy of this presentation.
You don’t have to ……….
Notes: This slide needs update with new QR Code

## Slide 44
Any Questions?