## Slide 1
RIST Relay Overview
Ciro A. Noronha, Ph.D.
Cobalt Digital

## Slide 2: What is the Problem?
RIST Client wants to connect to RIST Server
Firewall at the client side is not a problem – it is an outgoing connection
Firewall at the server side will not let the connection in
  That’s what firewalls are for!
  IT department will need to open and forward one more ports to allow this to happen
Can we make this work without having to involve IT? Just like Skype?
RIST Client
RIST Server
Internet
Firewall
Firewall

## Slide 3: Generic Solution
RIST Client
RIST Server
Internet
Firewall
Firewall
Use a server out on the Internet to “help” the endpoints communicate.
The “RIST Relay” (RR)

## Slide 4: Why RIST?
Users have explicitly requested mechanisms to simplify firewall crossing for RIST streams
  RIST devices may be “guests” on some third-party network
Advantages of a common Specification:
  Mix-and-match of clients, servers and relay points
  Vendors can create innovative solutions
  Multiple business opportunities:
    Provide the software
    Provide a server
    Provide a service

## Slide 5: Why not STUN/TURN/ICE?
There are RFCs that provide this functionality (ICE, aided by STUN/TURN) – what is wrong with that?
These are not complete solutions:
  STUN allows a node to figure out its public address
  TURN is a relay server in case you can’t go directly
  ICE is a means to negotiate STUN/TURN
  You still need something like a SIP server so the nodes can discover each other
  STUN/TURN have possible security issues
For security, it is necessary to combine all the functions (STUN/TURN/ICE plus a server) into a single server.
The RIST AG elected to re-use the RIST security and design a complete solution using Advanced Profile.

## Slide 6: A Closer Look at Firewalls
As far as traffic management goes, there are two types of NAT firewalls:
  Asymmetric Firewalls:
    Outgoing traffic creates a temporary rule that includes only the port
    Any return traffic matching the port is admitted into the network
    Most consumer-grade firewalls are asymmetric
    Direct bypass is possible
  Symmetric Firewalls:
    Outgoing traffic creates a temporary rule that includes both IP address and port
    Only return traffic from that IP address is admitted into the network
    Higher security
    Direct bypass is not possible

## Slide 7: Asymmetric Firewalls Allow Bypass
From IB:PB To IF:PF
From IF:PF To IS:PS
Device A
Server IP: IS
Port: PS
Device A IP: IA
Port: PA
Firewall IP: IF
Internet
From IA:PA To IS:PS
Rule: Packets to IF:PF are forwarded to IA:PA
Device B IP: IB
Port: PB
Device A can be reached at IF:PF
Device B

## Slide 8: Symmetric Firewalls Block Bypass
From IB:PB To IF:PF
From IF:PF To IS:PS
Device A
Server IP: IS
Port: PS
Device A IP: IA
Port: PA
Firewall IP: IF
Internet
From IA:PA To IS:PS
Rule: Packets to IF:PF from IS are forwarded to IA:PA
Device B IP: IB
Port: PB
Device A can be reached at IF:PF
Device B

## Slide 9: Firewall Implications
Asymmetric Firewalls allow endpoints to connect directly
  Very desirable from a bandwidth point of view
  Server is only involved in connection establishment
  Lower security in the firewall
Symmetric Firewalls only allow endpoints to connect to a server
  Server must be capable of relaying the content from endpoint to endpoint as direct communication is not possible
  This is why we called it the “RIST Relay”

## Slide 10: RIST Relay (RR) Requirements
Endpoints must “login” and be authenticated by the RR since:
  RR “works around” a firewall, so security is very important
  Only registered and allowed endpoints should be permitted
  Since endpoints can connect from anywhere, the RR must provide some sort of directory service to allow end-to-end connections
RR must be able to facilitate direct bypass connections
  There is no way to “know” if bypass is going to work until it is tried
RR must be able to relay (forward) traffic between endpoints
Endpoints should have some control of what happens

## Slide 11: RIST Relay Security
Endpoints must establish a RIST Advanced Profile connection with both encryption and authentication:
  DTLS with certificate-based authentication
  DTLS with TLS-SRP (username/password authentication)
  PSK with EAP-SHA256-SRP-6 (username/password authentication)
  Wireguard (in the publication queue as TR-06-4 Part 2)
The authentication information identifies the endpoint to the RR
Endpoints are identified by a human-readable name, pre-configured in the RR using out-of-band means

## Slide 12: Quick Recap of RIST Advanced Profile
RIST Advanced Profile is published as TR-06-3
Advanced Profile basics:
  It provides a tunnel encapsulated in RTP
  It provides packet loss protection via ARQ and/or FEC to the tunnel
  It supports multiple encryption and authentication options
  It supports encapsulation of multiple protocols, including IPv4/v6, Ethernet, GRE, as well as a direct payload option
  It includes a control channel, also encapsulated in RTP, with a custom packet format

## Slide 13: RR Communication Protocol
Communication with the RR is via Advanced Profile Control Messages
  New set of messages defined for RR use
  Messages not protected by ARQ, the protocol takes into account possibility of packet loss
Messages are encrypted
RR can say “no” to requests
RIST keep-alive messages are used to keep the connection active
Control Index | Message | Mandatory
0x8030 | Connection Initiation Message | Yes
0x8031 | Request Denied Response | Yes
0x8032 | Directory List Response | RR only
0x8033 | Connection Request Response | Yes
0x8034 | Connection Incoming Message | Yes
0x8035-0x803F | Reserved for RR-to-Endpoint Control Messages | 
0x8040 | Connection Initiation Response | Yes
0x8041 | Connection Incoming Response | Yes
0x8042-0x804F | Reserved for Endpoint-to-RR Control Messages | 

## Slide 14: General Operation
At connection, the endpoint receives one of the following:
  “RR is ready”
  “RR is busy, go away”
  “Redirect to some other RR” (specified by IP address or hostname)
After an endpoint successfully connects to the RR, it indicates:
  “I wish to connect to some other endpoint”
  “I am ready to accept connections”
  “Give me the directory list of connected endpoints”
  “I am not yet ready to do anything”

## Slide 15: RR Can Say “No” (Request Denied)
The RR can say “no” to any request from the endpoint using the Request Denied message
The Request Denied message includes information to identify the request, and a reason code
  Unspecified reason
  Unauthorized
  Not Found (endpoint exists but is not currently connected)
  Does Not Exist (requested endpoint does not exist)
  RR Out of Resources
  Connection Refused by the Remote Endpoint
  Invalid Request
  Incompatible Protocol
  Invalid Requester IP Address

## Slide 16: Endpoint Protocol Support
Advanced Profile has multiple inner protocol options
Endpoint must declare which options it supports
Endpoint must indicate whether it is willing to accept bypass
RR can relay data packets across different encryption modes, but the actual data is opaque to the RR
The support information is part of the Connection Initiation Response from the endpoint
The support information is returned in the directory

## Slide 17: Protocol Support Flags
IPv4 bypass support
IPv6 bypass support
PSK support
DTLS support
Wireguard support
ARQ support
ST 2022-1 FEC support
ST 2022-5 FEC support
Ethernet Encapsulation support
Media-TS Encapsulation support
IPv4 Encapsulation support
Main Profile Encapsulation support
IPv6 Encapsulation support
Media-ST2110 Encapsulation support
Media-ST2022-6 Encapsulation support
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|B|V|P|D|W|A|C|E|F|S|R|M|T|U|I|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
This information is sent by the endpoint to the RR at connection initiation and returned as part of a directory query

## Slide 18: The “Blob”
When an endpoint registers with the RR, it may optionally include an ephemeral “blob” of data
  The “blob” only exists while the endpoint is connected
If another endpoint asks to connect to this endpoint, the RR will pass along the “blob” to the requesting endpoint
Defined “blob” types:
  Endpoint certificate in PEM format
  CA certificate in PEM format
  Concatenation of CA and endpoint certificates in PEM format
Vendor-proprietary blobs are supported but discouraged

## Slide 19: Multipoint Operation
The RR supports multipoint-to-multipoint operation by using groups
A group is identified by a name just like an endpoint
  Groups are created manually through out-of-band means
  Directory listings have a bit to indicate whether a name is an individual endpoint or a group
The RR is responsible for replicating received data to all other group members

## Slide 20: Multipoint Implementation Options
Full Proxy
  RR terminates Advanced Profile connections with all endpoints, including packet loss recovery
  Maximum ARQ bandwidth efficiency and lowest latency
  RR can provide format conversion if desired
Transparent
  RR simply forwards Advanced Profile payloads from sender to all receivers
  Packet loss recovery is end-to-end
  Bandwidth-inefficient and worst-case latency
Partial proxy cases are also possible

## Slide 21: Directory Query
Endpoints can ask the RR for a directory of connected endpoints
Responses include:
  Endpoint Name
  Endpoint Type (individual or group)
  Endpoint Protocol Support Flags
Directory access control and filtering are up to the RR and will not be part of the Specification

## Slide 22: Concurrent Connections
An endpoint is allowed to have multiple “idle” or “ready to receive” connections to the RR
  Used for redundancy
If the RR receives a connection request to this endpoint, it will choose one of the “ready to receive” connections at its discretion
  Protocol Support Flags may be used to inform this choice
Each endpoint is listed only once in the directory

## Slide 23: Protocol Exchange: Connecting to the RR
Endpoint
RIST Relay
Advanced Profile Authenticated Connection
Connection Initiation Message
RR Ready, your name is “xxx”
RR Busy, go away
Redirect to another RR
Connection Initiation Response
Directory Request
Connect to “yyy” endpoint
Not ready yet, stay idle
Ready to receive connections
Includes protocol support flags
Connection Initiation Response can be sent again at some later time to change the status of the endpoint

## Slide 24: Protocol Exchange: Connecting to Endpoint
XXX Endpoint
RIST Relay
YYY Endpoint
Connection Initiation Response
Connect to “YYY” endpoint
Connection Incoming Message
“XXX” endpoint wants to connect
Will use bypass or use the RR
Connection Incoming Response
Connection is accepted
Connection Request Response
Connect to “YYY” through the RR or Connect to “YYY” using this IP/port

## Slide 25: Protocol Exchange: Connecting to Endpoint
XXX Endpoint
RIST Relay
YYY Endpoint
Connection Initiation Response
Connect to “YYY” endpoint
Connection Incoming Message
“XXX” endpoint wants to connect
Will use bypass or use the RR
Connection Incoming Response
Connection is rejected
Request Denied Response
Connection refused by remote endpoint

## Slide 26: Conclusions
The RIST Relay RR will simplify support for establishing RIST connections for endpoints behind firewalls
By using a common Specification, one can mix-and-match RR and endpoint vendors
Specification will only include the minimum for interoperability, allowing vendors to innovate
This is still work in progress and no implementations exist yet

## Slide 27
Any Questions?