## Slide 1
PTP: The Key to ST 2110 Timing
Andrew Scott, Telestream

## Slide 2: Precision Time Protocol – History
Designed to synchronize clocks via a computer network, with much higher accuracy than NTP
Widely used in industries such as telecom and finance, now being adopted for video applications to replace analog sync
Version 1 published as IEEE 1588-2002, not used for video
Version 2 published as IEEE 1588-2008
  Updated with IEEE 1588-2019 (“Version 2.1”)
Augmented with standards such as SMPTE ST 2059-2 (since 2015)
Some terminology has changed: Master/Slave  Leader/Follower

## Slide 3: PTP over IPv4
User Datagram Protocol (UDP) used for transport
  Port 319 for Event messages
  Port 320 for General messages
Multicast group address for most messages: 224.0.1.129
Exchange of PTP messages may be multicast, unicast, or a mix of both

## Slide 4: Common PTP Message Types
Event message class
  Sync
  Delay_Req
General message class
  Announce – used to establish the synchronization hierarchy
  Delay_Resp
  Follow_Up
  Management – used to query and update “data sets” used by PTP instances
Differentiated Services used by switches to enforce high priority for event messages

## Slide 5: Clock Synchronization
Sync messages sent periodically (e.g. 8 per second) from leader to followers
Follow_Up message needed only if Sync timestamp is not included in the Sync message
Followers send Delay_Req, typically at same rate as Sync
After complete exchange, followers have all 4 timestamps

## Slide 6: Clock Synchronization
Follower clock can be adjusted using these values
There is also a provision for asymmetric network delays

## Slide 7: PTP Clock (Node) Types
Ordinary Clock
  PTP nodes with a single port on the network
  Can be either a follower or a leader
  Typically in video networks, we have grandmaster (GM) clocks that are leader-only and devices (cameras, etc.) that are follower-only
Boundary Clock
  Multi-port device (i.e. switch) with one follower (synced to the GM) and many leaders on all other ports
  Provides scalability in large PTP networks
Transparent Clock
  Switch that updates timestamps in PTP messages but does not assume a role

## Slide 8: Media Network Architecture
Redundant network for resiliency
Leaf/Spine switches (boundary clocks) for scalability
Hybrid facility with PTP  analog to support legacy devices
Spine
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Spine
Amber (primary) network
Blue (backup) network
Camera
Display
PTP Only
Analog Sync Signals
Legacy Devices
Sync Gen Grandmaster
GNSS
Media Node

## Slide 9: Lead Clock Determination
Announce messages are sent periodically (typ. 1 per second) and include (in priority order):
  Priority 1 – user-configured
  Clock Class – GNSS locked, holdover, free-running, etc.
  Clock Accuracy – estimate based on time source, e.g. “within 25 ns”
  Clock Variance – computed stability of local clock
  Priority 2 – user-configured
  Clock Identity – (tie-breaker) based on MAC address
Potential leaders use the Best Master Clock Algorithm (BMCA) to decide which node is the sync source

## Slide 10: Best Master Clock Algorithm
Leader clocks listen for other Announce messages
Start sending Announce when better than received Announce
  Or when no Announce received (timeout is usually 3s)
Stop sending Announce (go to Passive) when a better leader is seen
Power On, Reset
Listen
Passive
Grandmaster
Announce from
better leader
No announce from
better leader
No announce from
better leader
Announce from
better leader

## Slide 11: PTP Domains
Domain is simply a numeric identifier (0-255) for a logical PTP network
Multiple domains can co-exist on a physical network
  For example, separate audio (AES67) and ST 2110 domains
Every PTP message includes the domain number so nodes can accept or discard the message as appropriate

## Slide 12: PTP Profiles
A profile is a set of PTP options and attributes for a given application
  Message rate defaults and permitted limits (Announce, Sync, etc.)
  Communication models (e.g. multicast, unicast, mixed)
IEEE 1588-2019 specifies the “Delay Request-Response Default PTP Profile”
SMPTE 2059-2:2021 specifies the “SMPTE profile for synchronization in a professional broadcast environment”
AES67-2018 specifies the “PTP profile for media applications”
Other profiles for telecom and other applications

## Slide 13: SMPTE 2059-2
Specifies the PTP profile used by ST 2110
Permits three communication models:
  Multicast for all messages
  Unicast for all messages. Followers are configured with a list of potential leaders and use a “grant” mechanism to request that the leader send unicast Announce, Sync, and Delay_Resp messages
  Mixed – Announce, Sync (& Follow_Up) and Management messages are sent by multicast. Delay_Req/Delay_Resp are sent by unicast (without grant)
Adds a synchronization metadata TLV in Management messages to signal time code information to media nodes (e.g. next jam time)

## Slide 14: Best Practices
Create a solid network plan
  Redundant amber/blue networks
  Switches that support PTP, ideally Boundary Clock mode
  Scalable switch architecture – Spine/Leaf
Use PTP-only link between amber/blue networks so that GMs can see each other’s Announce messages
  All devices see the same GM on both networks
Configure switch ports “role master” to prevent rogue leaders
Use SMPTE 2059-2 profile and default message rates
  Use Mixed Multicast/Unicast communication model

## Slide 15: Troubleshooting Tools
PTP monitoring and measurements
Wireshark packet captures for offline analysis

## Slide 16
Any Questions?