## Slide 1
IP Showcase ST 2110 LaunchPad
Wes Simpson, Founder, LearnIPvideo.com
LearnIP
video.com

## Slide 2: Key Requirements for IP Video Systems
Function | Description | Standards
Encapsulation | Put media data into IP packets | Video: ST 2110-20 Audio: ST 2110-30 & AES67 Ancillary Data: ST 2110-40

## Slide 3: Key Requirements for IP Video Systems
Function | Description | Standards
Encapsulation | Put media data into IP packets | Video: ST 2110-20 Audio: ST 2110-30 & AES67 Ancillary Data: ST 2110-40
Synchronization | Align media streams to a common clock | IEEE 1588 PTP – Precision Time Protocol ST 2059 and ST 2110-10

## Slide 4: Key Requirements for IP Video Systems
Function | Description | Standards
Encapsulation | Put media data into IP packets | Video: ST 2110-20 Audio: ST 2110-30 & AES67 Ancillary Data: ST 2110-40
Synchronization | Align media streams to a common clock | IEEE 1588 PTP – Precision Time Protocol ST 2059 and ST 2110-10
Switching and Routing | Move packets from one device to another | IGMPv3 Multicasting

## Slide 5: Key Requirements for IP Video Systems
Function | Description | Standards
Encapsulation | Put media data into IP packets | Video: ST 2110-20 Audio: ST 2110-30 & AES67 Ancillary Data: ST 2110-40
Synchronization | Align media streams to a common clock | IEEE 1588 PTP – Precision Time Protocol ST 2059 and ST 2110-10
Switching and Routing | Move packets from one device to another | IGMPv3 Multicasting
Connection Management | Route signals from sources to destinations | SDP – Session Description Protocol NMOS IS-05

## Slide 6: Media Transport over IP
SMPTE ST 2022-6
SMPTE ST 2110

## Slide 7: The IP Video Ecosystem
Replace text box with image.
Delete side panel if image is too large to fit inside text box.

## Slide 8: IP Media Evolutionary Tree
Uncompressed
Compressed
Pro-MPEG CoP3
ST 2022-1,2
TR-01
ST 2022-3,4
RFC 4175
AES 67
TR-03
TR-04
ST 2022-5,6
RFC 8331
ST 2110
ST 2110-10
ST 2110-20
ST 2110-30
ST 2110-40
ST 2110-21
ST 2022-7
ASPEN
RDD 37
ST 2022-8
ST 2110-31
RP 2110-23
ST 2110-22
RIST
TR-07
TR-08
IPMX
RP 2110-24
>> Note that ALL these signals could co-exist on the SAME IP network <<

## Slide 9: SMPTE ST 2022-6
Specifically designed for transporting SDI signals over IP
  270 Mbit/s, 1.485 Gbit/s and 2.97 Gbit/s
Carries entire SDI signal intact
  Video, embedded audio, ancillary data, HANC, VANC and all other bits
  Permits bit-for-bit copy of signal to be transported across IP network
Works with ST 2022-5 Forward Error Correction
  Row/Column FEC handles lost RTP datagrams
  Separate UDP ports used for transmission of SDI and FEC

## Slide 10: Media Transport over IP: SMPTE ST 2022-6
Take entire SDI signal and encapsulate into one IP stream
  Includes audio and embedded data signals
Easy to maintain audio/video synchronization
  Hard to process just one part of a stream
IP Packet Network
SDI
Video
Audio
Embed
Data
Packetize
De-embed
De-packet
SDI
Video
Audio
Data
ST 2022-6 IP Packets
Video/Audio/Data

## Slide 11: SMPTE ST 2110
General-purpose media transport over IP
  Standards for video, audio, synchronized metadata
Carries each media element as a separate stream
  Video in one stream, one or more audio channels in another, metadata in another
Capable of handling wide variety of formats
  Video from SD all the way up to 8K HDR and beyond
  Compressed and uncompressed video at any frame rate
  Multi-channel audio at multiple sampling rates
  Many different categories of metadata

## Slide 12: Media Transport over IP: SMPTE ST 2110
Each media type in a separate packet stream
  Easy to process individual components
  Signals need to be resynchronized after processing
PTP (Precision Time Protocol) used for packet timestamping
SDP Files used to describe each packet stream
IP Packet Network
SDI
Video
Audio
Data
SDI
Video
Audio
Data
Packetize
ST 2110-20 Video
De-packetize
ST 2110-40 Data
ST 2110-30 Audio
SDP Files

## Slide 13: ST 2022-6 / ST 2110 Audio Processing Packet Flow
IP Packet Network
SDI
Video
Audio
Embed
Data
Packetize
De-packet
Packetize
De-embed
Audio
Processing
Embed
De-embed
De-packet
SDI
Video
Audio
Data
SMPTE 2022-6 IP Packets
Video/Audio/Data
Using SDI/ST 2022-6
Using ST 2110
IP Packet Network
SDI
Video
Audio
Data
SDI
Video
Audio
Data
2110-30
Audio
Packetize
Audio
Processing
De-pack/Pack
ST 2110-20 Video
De-packetize
SDP Files

## Slide 14: SMPTE ST 2110 – Released Standards
OV 2110-0 Roadmap for the 2110 Document Suite
ST 2110-10 System Timing and Definitions
ST 2110-20 Uncompressed Active Video
ST 2110-21 Traffic Shaping and Delivery Timing for Video
ST 2110-22 Constant Bit-Rate Compressed Video
ST 2110-30 PCM Digital Audio (uncompressed)
ST 2110-31 AES3 Transparent Transport (for non-PCM audio)
ST 2110-40 SMPTE ST 291-1 Ancillary Data
ST 2110-43 TTML for Captions and Subtitles

## Slide 15: ST 2110-20 Video Encapsulation
Multiple video pixel groups (pgroups)
RTP Payload Header applied (unique to each media type)
Inserted into an RTP packet
Placed into UDP packet
IP packet header attached
Wrapped into Ethernet Frame
PH
RTP
UDP
IP
MAC
CS
pg
RTP Payload Header
pg
pg
pg
pg
pg
pg

## Slide 16: ST 2110-20 Pixel Groups
Pixels formed into pgroups
  pgroup size depends on sampling format
  Must be integer number of octets
  Pixels that share samples must be in the same pgroup
Example: 4:2:0 8-bit groups 4 pixels into 6 octets
Example: 4:2:2 10-bit groups 2 pixels into 5 octets
Cb’
Y’11
1
2
3
4
5
6
Cr’
Y’10
Y’01
Y’00
C’B
C’R
Y0’
Y1’
1
2
3
4
5

## Slide 17: ST 2110-20 Sample Row Data
Active Video
(e.g. 1920x1080)
Embedded Audio
(HANC)
Ancillary Data (VANC)
Packet 0
Packet 1
Packet 2
Packet 0
Packet 1
P 2
Packet 2
X
2X

## Slide 18: Lossless Compression
Visually lossless compression cannot be seen by observer
  Some data must always be removed
  Done so as to be invisible to human viewer
  Can have very low latency (~1 millisecond or less, encode + decode)
Popular codecs available
  JPEG XS – RTP Encapsulation – RFC 9134
  Also VC-2 DIRAC from BBC – RFC 8450
2:1 to 8:1 compression ratio
  3Gbit/s SDI compressed to 1.5 to 0.5 Gbit/s

## Slide 19: Compressed Video Signal Rates
Often measured in bpp (bits per pixel)
Uncompressed SDI used 4:2:2 10-bit video
  Works out to 20 bits/pixel
  Note that SDI also has HANC and VANC occupying significant bandwidth
Video Format | Pixels/frame | Pixels/second | “SDI” bit rate | 1 bpp | 3 bpp | 6 bpp
720p60 | 921,600 | 55,296,000 | 1.485 Gbit/s | 70 Mbit/s | 195 Mbit/s | 390 Mbit/s
1080i60 | 2,073,600 | 62,208,000 | 1.485 Gbit/s | 70 Mbit/s | 195 Mbit/s | 390 Mbit/s
1080p60 | 2,073,600 | 124,416,000 | 2.97 Gbit/s | 150 Mbit/s | 390 Mbit/s | 780 Mbit/s
4K 2160p60 | 8,294,400 | 497,664,000 | 11.88 Gbit/s | 500 Mbit/s | 1.4 Gbit/s | 2.8 Gbit/s
8K 4320p60 | 33,177,600 | 1,990,656,000 | 47.53 Gbit/s | 2 Gbit/s | 5.6 Gbit/s | 11.2 Gbit/s

## Slide 20: ST 2110-30 Audio Encapsulation
96 ea. 24 bit Samples (3 bytes) @ 96 kHz
0
2
4
95
0
0
0
0
1
1
1
1
95
95
95
95
1 msec
RTP
UDP
IP
One ST 2110-30 Packet
1
3
2
2
2
2
Each Channel has 3 x 96 = 288 bytes per packet
4 Channels have 4 x 288 = 1,152 bytes
All channels in one IP Packet
Maximum theoretical capacity – 5 channels, 1440 bytes
4 channels of 96 kHz 24-bit audio

## Slide 21: 2110-40 Ancillary Data
Extract ancillary ST 291 data packets from VANC or HANC
  Captions, time code, ad triggers, etc.
  Place them into RTP packets with custom header
Line numbers are based on SDI line numbering
  Don’t match 2110-20 line numbers
000 3FF 3FF
41
07
Ancillary Flag
DID
SDID
xx
DC
SCTE 104
zz
CS
User Data
ANC Data
Packet
Line #, Offset
41
07
Anc. Packet Header
DID
SDID
xx
DC
SCTE 104
zz
CS
User Data
RTP
Datagram
01
Payload Hdr.
Seq. #, SSRC
RTP Header

## Slide 22: IP Transport
RTP Encapsulation
Timing

## Slide 23: RTP Packet Features
Payload Type
Time Stamp
X
P
V
16 Bits
M
CC
RTP Sequence Number (low 16 bits)
Synchronization Source
(SSRC) Identifier
RTP Header
M-Bit – Media-specific indicator flag
In ST 2110 video, indicates last packet of video frame
Sequence number
  Each packet in a stream has a unique number
  Permits packets to be put into correct sequence
  Allows missing packets to be detected
Payload Type
Indicates type of media in packet (video/audio/etc.)
Timestamp
  Indicates when media content was created
  Multiple packets may share one timestamp

## Slide 24: All Signals in Phase at SMPTE Epoch
t=0
t=20
t=40
t1
t2
SMPTE Epoch – Jan. 1, 1970, 00:00:00 TAI
Other signals
tied to SMPTE Epoch
50 Hz
video
Current time
Next
alignment point

## Slide 25: ST 2110-20 RTP Timestamps and Sequence Numbers
All packets from one video frame will have the same RTP timestamp
  However, RTP Sequence number is always incremented by one for each packet
  For interlaced video, the packets for each field will have the same timestamp
Timestamp will jump for each frame of video
  By a count equal to the clock rate (90 kHz) divided by the video frame/field rate
TS = 20000
Seq. = 7999
TS = 21800
Seq. = 8000
TS = 21800
Seq. = 8001
TS = 21800
Seq. = 11999
TS = 23600
Seq. = 12000
TS = 21800
Seq. = 8002
Frame N
Frame N+1
Frame N+2

## Slide 26: 500 Mbps Signal on a 10 Gbps Link
Chart: 
 | 0 | 0 | 0 | 10000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10000 | 0 | 0 | 0 | 0 | 0 | 0
10 kbit packets for
1 microsecond
19 microsecond gap

## Slide 27: Two 2.5 Gbit/s Signals on Two 10 Gbps Links
Chart: Video 1
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41
Video 1 | 10000 | 10000 | 10000 | 10000 | 10000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10000 | 10000 | 10000 | 10000 | 10000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10000 | 10000
Chart: Video 2
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41
Video 1 | 10000 | 10000 | 10000 | 10000 | 10000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10000 | 10000 | 10000 | 10000 | 10000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10000 | 10000
Switch buffers will overflow if muxed
onto a single link
Two signals will collide
if both are burst-mode

## Slide 28: Type N, NL and W Packet Pacing
VANC
Type NL
Type N
Type W
Bit Rate
Variation
Bit Rate
Variation
Bit Rate
Variation
Packet
Moving Average
Bit Rate

## Slide 29: ST 2022-7 Hitless Protection Switching
Send identical signal on two separate paths
  Identical RTP packet timestamps, RTP sequence numbers
  Receiver aligns packets using buffer
  Transit time equal to delay of longest path
SMPTE ST 2022-7 Standard
  “Seamless Protection Switching of RTP Datagrams”
  Published in 2019
Source
Destin-
ation
Path A
Path B

## Slide 30: SDP Example for 1080i 29.97Hz Video
v=0
o=wes 203763372 89 IN IP4 10.201.33.19
s=Example of a 1080i29.97 video signal
t=0 0
m=video 31008 RTP/AVP 101
c=IN IP4 232.201.33.11/32
a=source-filter: incl IN IP4 232.201.33.11 10.201.33.19
a=rtpmap:101 raw/90000
a=fmtp:101 sampling=YCbCr-4:2:2; width=1920; height=1080; interlace; exactframerate=30000/1001; depth=10; TCS=SDR; colorimetry=BT709; PM=2110GPM; SSN=ST2110-20:2017
a=ts-refclk:ptp=IEEE1588-2008:39-A7-94-FF-FE-07-CB-D0:42
a=mediaclk:direct=0

## Slide 31: Multicast Stream Dynamics
Source offers stream via multicast addresses listed in SDP
  Destination devices get SDP via NMOS or other means
Receivers generate requests to join multicasts using IGMPv3
Network determines best way to deliver streams
SDP File

## Slide 32: ProAV Format Comparison
Capability/Feature | IPMX | ST 2110 | SDVoE | HDBaseT
Uncompressed 4K60p Video | Yes | Yes | No | No
Visually Lossless Compression | Yes | Yes | Yes | No
Network-based Precision Clock (PTP) | Optional | Required | No | No
Open Standard | In process | Yes | No | No
HDCP Support | Yes | No | Yes | Yes
ST 2110 Compatibility | Yes | Yes | No | No
IR Control Link | No | No | No | Yes
PoE (Power over Ethernet) | Possible | No | No | Yes
PoH (Power over HDBaseT) (100W) | No | No | No | Yes
Data Channel* | Not Required | Not Required | Up to 1 Gbit/s | Up to 100 Mbit/s
*IPMX and ST 2110 work over standard IP/Ethernet infrastructure. As such, other IP and Ethernet data flows can easily be transported over the same networks.

## Slide 33: So, Why ST 2110?
Futureproof
  Can handle any video format: 8K, HDR, 3D, and beyond
Cloud-Friendly
  IP signals travel easily to and from public and private clouds
Flexible
  Common network backbone handles SD, HD, UHD, SDR, HDR, multiple frame rates, compressed/uncompressed, streaming, file transport and much more

## Slide 34: Emmy-award Winning Technology

## Slide 35
Any Questions?
LearnIP
video.com