## Slide 1
Testing Controllers for NMOS Compliance
Rob Porter
Sony Europe B.V.

## Slide 2: Overview
JT-NM Tested event in August 2022 used automated controller testing for the first time
How did we get to this point?
  What is NMOS?
  What do we mean by a controller?
  What NMOS features should a controller support?
  What is the NMOS Testing Tool?
  How was automated controller testing added to the NMOS Testing Tool?
  How can I run the tests myself?
  How was it used at JT-NM Tested?
  What’s next for controller testing?

## Slide 3: What is NMOS?
Networked Media Open Specifications
  Set of open APIs for managing devices on professional media networks
  Allow interoperability between different manufacturers’ devices
  Use standard RESTful APIs using HTTP GET, PUT, PATCH, DELETE with JSON payloads and WebSocket for notifications of updates
IS-04 – Discovery and Registration
IS-05 – Connection Management
IS-06 – Network Control
IS-07 – Event and Tally
IS-08 – Audio Channel Mapping
IS-09 – System
IS-10 – Authorisation
BCP-002 – Grouping
BCP-003 – Security
BCP-004 – Receiver Capabilities

## Slide 4: What do we mean by a controller?
Controller
Node
Node Media endpoint on the network
Registry Database of Nodes on the network
Controller Allow users to view available Nodes and make connections
Registry
Node

## Slide 5: What NMOS features should a controller support?
Controller
Node
Node
IS-04 Registration API
IS-04 Query API
Registry
IS-04 Registration API
IS-04 Discovery & Registration

## Slide 6: What NMOS features should a controller support?
Controller
Node
Node
IS-05 Connection API
1
IS-05 Connection API
2
Registry
IS-05
Connection Management

## Slide 7: What is the NMOS Testing Tool?
Open source software
Freely available from AMWA GitHub site
Developed collaboratively by AMWA members
Ensures that professional media equipment conforms to the NMOS specifications correctly
Allows vendors, systems integrators and end users to self-test their equipment
Used at JT-NM Tested events
Key tool in the drive to better interoperability

## Slide 8: What is the NMOS Testing Tool?
IS-04 Node API
IS-05 Connection API
IS-04 Registration API
Operator
NMOS Node under Test
Mock Registries
Node Testing
Configure
Configure
NMOS Testing Tool

## Slide 9: How was automated controller testing added to the NMOS Testing Tool?
Q&A protocol
IS-04 Query API IS-05 Connection API
Mock Registry and Nodes
Operator
NMOS Controller under Test
Configure and operate
Configure
Answer questions
Controller Testing
NMOS Testing Tool
NMOS Controller Testing Façade

## Slide 11: How can I run the tests myself?
https://www.youtube.com/watch?v=cfVSSD9hQO4
(Search: NMOS Test Tool Tutorial on YouTube)
https://specs.amwa.tv/nmos-testing/
(Search: AMWA NMOS Test Tool on Google)

## Slide 12: How was it used at JT-NM Tested?
There have now been four JT-NM Tested events
Controller testing was introduced at the third event but was a manual process
Automated controller testing was introduced at this year’s event
JT-NM Tested Event | NMOS Node testing | NMOS Registry testing | NMOS Controller testing
March 2019 | No | No | No
August 2019 | Yes | No | No
March 2020 (Virtual) | Yes | Yes | Yes (Manual)
August 2022 | Yes | Yes | Yes

## Slide 13: What’s next for controller testing?
AMWA “NMOS Client Testing” activity
NMOS Architecture Review Group review and approve new test suite
AMWA workshop
JT-NM Tested event
AMWA “NMOS Controller Specification” activity
Publication of IS-04 v1.3.2 IS-05 v1.1.2 BCP-003-01 v1.0.1
Further Controller test suites
New sections on Controllers in NMOS specifications approved
September 2021
March 2022
August 2022
Controller testing roadmap
September 2022
Notes: The new Controller test suites currently test only some key IS-04 and IS-05 functionality for Controllers. To clearly define what else Controllers should be able to do, another AMWA activity was launched to provide better guidance for implementers. This “NMOS Controller Specification” activity resulted in the addition of clearly worded Controller sections to the IS-04, IS-05 and BCP-003-01 (transport layer security) specifications and the creation of a new implementation guide for Controllers, INFO-005. These documents will be used as the basis to provide further additions to the Controller test suites in future.
Controller testing
  Sony led an NMOS Controller Specification activity in AMWA to prepare clear guidance for Controller implementers
  This should lead to further Controller test suites in future
NMOS Testing Tool
  It’s an AMWA requirement of any NMOS activity to produce a test suite
  So more tests will be produced in future as the suite of specs expands
  New tests can also be introduced to address interoperability issues should any be discovered

## Slide 14: What’s next for controller testing?
Controller implementation guide
New Controller sections in specifications
IS-04
IS-05
BCP-003-01
INFO-005
https://specs.amwa.tv

## Slide 15
Any Questions?